Specifications For The 5020T

The machines are CE marked and meet all European emission and safety regulations.

Description

Jaw crusher with opening of 500mm x 200mm

Single toggle

Variable output sizes from 100mm down to 5mm

Material

The 5020 will crush concrete, kerbstones, granite sets, marble gravestones, paving slabs, old asphalt, bricks, blocks and any rock found in the UK.

Output

Maximum output per hour on 100mm setting is 20 TPH, based on clean concrete. Soft bricks or blocks reduce this output. Remove wood and clay as these clog the jaws.

Jaws

Hydraulically adjusted, just at the touch of a lever. Quick release if a jam occurs. Will crush hardest rock of 400 kilonewtons. If the jaws encounter steel, they will just stop on the hydraulic pressure release. Flicking the lever into reverse will release the steel easily.

The jaw plates are 12% manganese and will work harden. They should last for 2 years on general rubble. On hard or abrasive rock, they will last from 6 to 12 months. The jaws are reversible and cost of replacement is £300 each.

Engine

The engine is a Yanmar 25HP water-cooled diesel. Max speed 3600rpm. It is set at 2600 rpm for quiet running. A full tank of diesel will last for 10 hours. It is very economical, using only 3 litres of diesel per hour. The engine is fitted with a cyclonic dust filter.

Tracks and Controls

Tracks are rubber but steel tracks can be fitted for £600. The crusher will climb a 30-degree incline and turn full circle on the same spot. Controls are hydraulic lever type, simple and easily maintained. The hydraulics are standard equipment which can be purchased off the shelf. An oil cooler is fitted to ensure longer life of hydraulic equipment and for hotter days or climates. Remote controls can be offered if required.

Conveyor and Dust Suppression

The conveyor is simple in design with few parts. There are no bed rollers to seize up or cause tracking problems. The belt is moulded in one piece and is thus much stronger and reliable and is easy to fit. The speed of the belt is adjustable. The conveyor can be easily removed if there is heavy re-bar being put through the machine.Dust suppression is by means of fine water spray nozzles on the conveyor, using a standard domestic hose fitting.

Screener

An optional screener is available. This will accept various decks from 5mm mesh to 35 mm. The screener takes a few minutes to attach.

Safety and Maintenance

There are two emergency cut out switches, one on each side of the machine. All doors have safety switches. The machine has easy access for maintenance and cleaning. Oil changes and greasing should be carried out every 500 hours.

Loading

Maximum productivity is achieved by correct loading of the crusher. The most effective is with a maximum 3 ton, 360 excavator fitted with an 18" bucket. The hopper must not be swamped. The machine should be loaded at a constant rate that the crusher can accept.